Static and touring holiday use caravan park standards

Introduction

1. 	Under section 5(6) of the Caravan Sites and Control of Development Act 1960 (the Act) the Secretary of State may from time to time specify model standards with respect to the lay-out and the provision of facilities, services and equipment for caravan sites or particular types of caravan site; and that, in deciding what (if any) conditions to attach to a site licence, the local authority shall have regard to any standards so specified.

2. 	These standards only apply to those sites which contain caravans that are used for Holiday use only static or touring. They do not apply to sites used exclusively for holidays or touring caravan sites (for which separate model standards have been issued). The standards also do not apply to sites occupied by gypsies or travelers or caravan sites which house agricultural workers.

Previous Standards

3. 	The 2008 Standards replace the document “Model Standards 1989: Permanent Residential Mobile Homes Sites”. When issuing any new licenses or reviewing current ones the local authority must have regard to the 2008 Standards in setting or varying any of the conditions attached that consist of caravans used for Residential use.

Holiday occupancy condition

4.	The caravans and lodges on the site shall be used for holiday accommodation 	only and shall not be used for any other purpose.

In particular, the accommodation shall not be used as the sole or principal 	residence by any of the occupants.

The owners and operators of the site shall maintain an up-to-date register of 	the owners and occupiers of individual caravans and lodges and of their main 	home addresses (verified by a Council Tax Bill and photo ID/ driving licence) 	and shall make this information available at all reasonable times to the Local 	Planning Authority.

THE STANDARDS

1. The Boundaries and Plan of the Site

(i)	The boundaries of the site from any adjoining land shall be clearly marked by a man made or natural feature.

(ii)	No caravan or combustible structure shall be positioned within 3 metres of the boundary of the site.

(iii)	(a)	A plan of the site shall be supplied to the local authority upon the application for a licence and, thereafter whenever there is a material change to the boundaries or layout of the site, or at any other time on the demand of the local authority.

(b)	The plan supplied must clearly illustrate the layout of the site including all relevant structures, features and facilities on it and shall be of suitable quality.

2. Density, Spacing and Parking Between Caravans

(i)	Except in the case mentioned in sub paragraph (iii) and subject to sub paragraph (iv), every caravan must where practicable be spaced at a distance of no less than 6 metres (the separation distance) from any other caravan which is occupied as a separate residence.

(ii)	No caravan shall be stationed within 2 metres of any road or communal car park within the site or more than 50 metres from such a road within the site.

(iii)	Where a caravan has retrospectively been fitted with cladding from Class 1 fire rated materials to its facing walls, then the separation distance between it and an adjacent caravan may be reduced to a minimum of 5.25 metres.

(iv)	In any case mentioned in subparagraph (i) or (iii):

- A porch attached to the caravan may protrude one metres into the separation distance and must not exceed 2 metres in length and 1 metres in depth. The porch must not exceed the height of the caravan. Where a porch is installed only one door may be permitted at that entrance to the Caravan, either on the porch or on the caravan.

(b)	Eaves, drainpipes and bay windows may extend into the separation distance provided the total distance between the extremities of two facing caravans is not less than 5 metres, except where sub paragraph (iii) applies in which case the extension into the separation distance shall not exceed 4.25 metres.

(c)	A garage or car port may only be permitted within the separation distance if it is of non-combustible construction.

(d)	Fences and hedges, where allowed and forming the boundary between adjacent caravans, should be a maximum of 1 metres high.

(e)	Private cars may be parked within the separation distance provided that they do not obstruct entrances to caravans or access around them and they are a minimum of 3 metres from an adjacent caravan.

(v)	The density of caravans on a site shall be determined in accordance with relevant health and safety standards and fire risk assessments.

3. Roads, Gateways and Overhead Cables

(i)	Roads shall be designed to provide adequate access for emergency vehicles and routes within the site for such vehicles must be kept clear of obstruction at all times.

(ii)	New roads shall be constructed and laid of suitable bitumen macadam or concrete with a suitable compacted base.

(iii)	All roads shall have adequate surface water/storm drainage.

(iv)	New two-way roads shall not be less than 3.7 metres wide, or if they are designed for and used by one-way traffic, not less than 3 metres wide.

(v)	One-way systems shall be clearly signposted.

(vi)	Where existing two-way roads are not 3.7 metres wide, passing places shall be provided where practical.

(vii)	Vehicular access and all gateways to the site must be a minimum of 3.1 metres wide and have a minimum height clearance of 3.7 metres.

(viii)	Roads shall be maintained in a good condition.

(ix)	Cable overhangs must meet the statutory requirements.

4. Footpaths and Pavements

(i)	Every caravan shall be connected to a road by a footpath with a hard surface which shall be maintained in good condition.

(ii)	Where practicable, communal footpaths and pavements shall not be less than 0.9 metres wide.

5. Lighting

Roads, communal footpaths and pavements shall be adequately lit between dusk and dawn to allow the safe movement of pedestrians and vehicles around the site during the hours of darkness. Lights must be low level and downward facing so not to create a nuisance to others

6. Bases

(i)	Every static unit must stand on a concrete base or hard standing. Touring bases must support the Caravan in a safe and secure manor in adverse weather conditions.

(ii)	The base must extend over the whole area occupied by the unit and must project a sufficient distance outward from its entrance or entrances to enable occupants to enter and leave safely. The hard standings must be constructed to the industry guidance, current at the time of siting, considering local conditions.

7. Maintenance of Common Areas, including Grass, Vegetation and Trees

(i)	Every part of the site to which the public have access shall be kept in a clean and tidy condition.

(ii)	Every road, communal footpath and pavement on the site shall be maintained in a good condition, good repair and clear of rubbish.

(iii)	Grass and vegetation shall be cut and removed at frequent and regular intervals.

(iv)	Trees within the site shall (subject to the necessary consents) be maintained.

(v)	Any cuttings, litter or waste shall be removed from the immediate surrounds of a pitch.

8. Supply & Storage of Gas etc.

(i)	Gas (including natural gas) and oil installations, and the storage of supplies shall meet current statutory requirements, relevant Standards and Codes of Practice.

(ii)	Liquefied Petroleum Gas cylinders must not be positioned or secured in such a way as to impede access or removal in the event of an emergency.

9. Electrical Installations

(i)	On the site there shall be installed an electricity network of adequate capacity to meet safely all reasonable demands of the caravans and other facilities and services within it.

(ii)	The electrical network installations shall be subject to regulation under current relevant legislation and must be designed, installed, tested, inspected and maintained in accordance with the provisions of the current relevant statutory requirements.

(iii)	Any work on electrical installations and appliances shall be carried out only by persons who are competent to do the work being undertaken, in accordance with current relevant statutory requirements.

(iv)	Any work on the electrical network within the site shall be done by a competent person fully conversant with the appropriate statutory requirements.

10. Water Supply

(i)	All pitches on the site shall be provided with a water supply sufficient in all respects to meet all reasonable demands of the caravans situated on them.

(ii)	All new water supplies shall be in accordance with all current legislation, regulations and relevant British Standards.

(iii)	All repairs and improvements to water supplies and installations shall be carried out to conform with current legislation and British Standards.

(iv)	Work on water supplies and installations shall be carried out only by persons who are qualified in the work being undertaken and in accordance with current relevant legislation and British.

(v)	The site owners must have in place an emergency action plan to enable the provision of water in the event of any water supply being stopped or in the case of Private water supply it not available.

(vi)	Private water supplies must be tested, and results made available to the Local Authority on request.

11. Drainage and Sanitation

(i)	Surface water drainage shall be provided where appropriate to avoid standing pools of water.

(ii)	There shall be satisfactory provision for foul and wastewater drainage either by connection to a public sewer or sewage treatment works or by discharge to a properly constructed septic tank or cesspool approved by the local authority.

(iii)	All drainage and sanitation provision shall be in accordance with all current legislation and British Standards.

(iv)	Work on drains and sewers shall be carried out only by persons who are qualified in the work being undertaken and in accordance with current legislation and British or European standards.

12. Refuse Storage & Disposal

(i)	Where communal refuse bins are provided these shall be non-combustible and in a properly constructed bin store.

(ii)	All refuse disposal shall be in accordance with all current legislation and regulations.

13. Communal Vehicular Parking

Suitably surfaced parking spaces shall be provided to meet the requirements of Users of the site and their visitors.

14. Notices and Information

(i)	The name of the site shall be displayed on a sign in a prominent position at the entrances to the site together with the current name, address and telephone number of the licence holder and manager and emergency contact details, a copy of the site licence or the front page of the said licence and details of where the full licence and other information required to be available under this standard can be viewed and between which times (if not displayed on the notice board).

(ii)	A current plan of the site with roads and pitches marked on it shall be prominently displayed at the entrances to it.

(iii)	A copy of the current site licence shall be available for inspection in a prominent place on the site.

(iv)	In addition, at the prominent place the following information shall also be available for inspection at the prominent place:

(a)	A copy of the most recent periodic electrical inspection report.

(b)	A copy of the site owner’s certificate of public liability insurance.

(c)	A copy of the local flood warning system and evacuation procedures, if appropriate.

(d)	A copy of the fire risk assessment made for the site.

(v)	All notices shall be suitably protected from the weather and from direct sunlight.

16. Flooding

(i)	The site owner shall establish whether the site is at risk from flooding by referring to the Environment Agency’s Flood Map.

(ii)	Where there is risk from flooding the site owner shall consult the Environment Agency for advice on the likelihood of flooding, the depths and velocities that might be expected, the availability of a warning service and on what appropriate measures to take.

17. Requirement to Comply with the Regulatory Reform (Fire Safety) Order 2005

The site owner shall make available the latest version of the fire risk assessment carried out under the Regulatory Reform (Fire Safety) Order 2005 for inspection by residents and when demanded, a copy of the risk assessment shall be made available to the local authority.

18. Fire safety measures where the Regulatory Reform (Fire Safety) Order 2005 does not apply (such as single unit sites and those sites solely occupied by family groups)

(i)	The standards in this paragraph only apply if the site is not subject to the Regulatory Reform (Fire Safety) Order 2005.

Fire Points

(ii)	These shall be located so that no caravan or site building is more than 30 metres from a fire point. Equipment provided at a fire point shall be housed in a weather-proof structure, easily accessible and clearly and conspicuously marked “FIRE POINT”.

Fire Fighting Equipment

(iii)	Where water standpipes are provided:

(a)	The water supply shall be of sufficient pressure to project a jet of water not less than 5 metres from the nozzle.

(b)	There shall be a reel that complies with the current British Standard, with a hose not less than 35 metres long, having a means of connection to a water standpipe (preferably a screw thread connection) with a water supply of sufficient pressure and terminating in a small hand nozzle.

(c)	Hoses shall be housed in a red box and marked “HOSE REEL”. Access to the fire point shall not be obstructed or obscured.

(iv)	Where hydrants are provided, hydrants shall conform to the current British Standard.

(v)	Access to hydrants and other water supplies shall not be obstructed or obscured.

(vi)	Where standpipes are not provided or the water pressure or flow is not sufficient, each fire point shall be provided with water extinguishers 
(2 x 9 litres) which comply with the current British or European Standard.

Fire Warning

(vii)	A suitable means of raising the alarm in the event of a fire shall be provided at each fire point.

Maintenance and Testing of Fire Fighting Equipment

(viii)	All alarm and firefighting equipment shall be installed, tested and maintained in working order by persons who are qualified in the work being undertaken and be available for inspection by, or on behalf of, the licensing authority or the Fire and Rescue Service.

(ix)	A record shall be kept of all testing and remedial action taken.

(x)	All equipment susceptible to damage by frost shall be suitably protected.

Fire Notices

(xi)	A clearly written and conspicuous notice shall be provided and maintained at each fire point to indicate the action to be taken in case of fire. This notice should include the following:

“On discovering a fire:

I.	Ensure the caravan or site building involved is evacuated.

II.	Raise the alarm.

III.	Call the fire brigade (the nearest phone is sited at …….).”

Legal background

1.	The use of land as caravan sites is controlled by relevant planning legislation, whereas the physical standards and layout, amenities and other standards are controlled by a site licence issued under the Caravan Sites and Control of Development Act 1960 (“the Act”). Section 5 of the Act enables local authorities to set licence conditions.

2.	Under the Act, most privately owned sites must be licensed by the local authority, unless exempted under the Act. A licence will be granted unless the applicant does not have relevant planning permission to operate the site or has had a licence revoked in the last three years.

3.	The local authority may attach conditions to the licence, but these can only relate to the physical use of the site and its management. The Secretary of State may issue Model Standards which the local authority must have regard to in deciding what conditions to attach to a licence. The authority may from time to time alter a site licence condition (either of its own volition or upon the application of the licence holder).

4.	The local authority is required, under to maintain an accurate register of the site licenses in their area. Given the number of different types of sites that local authorities may deal with, it is recommended that the register shows what type of site each is, be it holiday, residential, mixed use or gypsy and traveler. It is recommended as a minimum the information the site register has is:

Name and address of site (if available the Geographic Information Service mapping code should also be logged)

Name of the licence holder, the site owner (if different) and any person managing the site on behalf of either of those persons

Type of site

The number of pitches

The licence conditions (if any)

The Boundaries and Plan of the Site

5.	The boundary should clearly define the limit of the site owner’s responsibility. The boundary should be suitably marked and properly maintained. This boundary could be formed of a fence, hedge, wall or natural feature or any other suitable structure (or any combination of these) or it may in whole, or part, be formed by an appropriate natural feature, such as a river or a wood. It would not normally be appropriate for that natural feature to simply include an open field.

6.	Plans of the site shall be provided to the local authority at the site owners’ expense.

7.	It is best practice for copies of the plan to be made available to the emergency services.

8.	The 3 metres separation distance inside the boundary serves the purpose of ensuring privacy from whatever is on the other side of the boundary, such as a road, and other developments, such as houses etc.

9.	The 3 metres separation distance measurement should be taken from the caravan wall.

# Footnotes

Section 2 and Schedule 1 to the Act set out in which circumstances a site licence is not required.

Section 5 (1) to (5). For restriction see Mixnam’s Properties v Chertsey UDC A.C. 735.

Section 5 (6).